## Slide 1: Master’s thesis presentation by Henrik Bergersen
Supervisors:
DTU: Bent Lauritzen, Amalia Chambon
AFRY: Jarl Robert Heer
26.02.2026

## Slide 2: Cogeneration of Power and Ammonia in Europe using Small Modular Pressurized Water Reactors
A Techno-Economic Analysis & Operational Strategy Optimization

## Slide 3: Table of contents
Background
Objective
Theory
Methodology
Results
Conclusion

## Slide 4: Background
Nuclear reactors operate most efficiently as baseload providers, where reducing output in response to price fluctuations leads to fuel underutilization. Giorgio Locatelli et al.
Cogeneration might serve as a mechanism to decouple the reactor power from grid demand and increase profitability. IAEA 2019
The ammonia market is a mature industry with 70% used for fertilizer, and additional expansion is projected into the low-carbon fuel sector. IEA 2021
Conventional ammonia synthesis relies on natural gas and offers opportunities for decarbonization. HydrogenEurope 2023
Small Modular Reactors have gained attraction in recent years for their potential lower upfront cost and site flexibility. IAEA 2024

## Slide 5: Objective
Investigate the techno-economic potential of deploying small modular pressurized water reactors for cogeneration of power and green ammonia within the European power market.
Power
Ammonia
SMR plant

## Slide 6: Theory on nuclear cogeneration

## Slide 7: Small modular pressurized water reactor
Illustration: djysrv 2020
iPWR is the most prominent type of SMR. C. Zeliang et al.

## Slide 8: Green ammonia synthesis
Haber Bosch
High-Temperature Steam Electrolysis
Image: S. Mitsushima et al.
Image: T. Smolinka

## Slide 9: Haber Bosch Process
Operates at high pressures and temperatures for process optimization
Hydrogen from electrolysis
Nitrogen from Pressure Swing Adsorption (PSA)
Catalytic reaction
Reactor

## Slide 10: High-Temperature Steam Electrolysis
Image: INL 2010
Replacing conventional Steam Methane Reforming with electrolysis
Uses steam for reduced electrical input (Gibbs energy)
Solid-Oxide Electrolysis Cells operates at 500-850ºC Kumar et al.

## Slide 11: Cogeneration
Cogeneration by diverting steam from the secondary steam loop. IAEA 2019
Continuous production of both power and ammonia to ensure operational stability. NEA 2011
Own illustration

## Slide 12: Cogeneration efficiency

## Slide 13: Cogeneration of power & green ammonia diagram
Small Modular Pressurized Water Reactor
Haber Bosch (Ammonia synthesis)
Electrolysis
Steam extraction
Steam
Reactors supply power to entire system

## Slide 14: Theory on techno-economic analysis

## Slide 15: Total revenues from power and ammonia

## Slide 16: Power prices in Europe
Ember 2025

## Slide 17: Ammonia prices in Europe
In 2025:
Blue ammonia 590 – 770 €/t
Green ammonia 800 – 1000 €/t
Source: businessanalytiq, Imarcgroup, SP-global
Data: Argus ammonia 2025

## Slide 18: Production costs
INL: literature review of advanced reactor cost estimates
Richard Turton et al. Analysis, Synthesis, and Design of Chemical Processes.

## Slide 19: Methodology
Thermodynamic model developed using DWSIM chemical process simulator
Simulated loads from 200 to 700 tons per day (tpd) of ammonia
Techno-economic analysis based on the marginal break-even electricity price using:
  Median values for the OPEX (38 €/MWh) and MOM (0.625) of SMRs.
  Operating cost of ammonia production estimated for a nominal capacity of 500 tpd.
Nuclear reactor supplies power to all process equipment
Capacity factor of 90%

## Slide 20: Reactor model based on European-SMR
Tandem 2023
European Small Modular Reactor (E-SMR) – Tandem Euratom project
Notes: Øyeblikksbildet av hva jeg ser på, men kan hende jeg dropper noen etterhvert

## Slide 21: Thermodynamic model
Secondary steam loop
Haber Bosch
HTSE
Multi-stage compression
Steam extracted before turbine train
Electrolysis feed water superheated to 230 C at 1 bar.
HTSE operated at 750 C and atmospheric pressure.
300 C
230
H2+N2
NH3
H2O

## Slide 22: Marginal Break-Even Electricity price
Generally:
Power revenues
Ammonia revenues

## Slide 23: Results

## Slide 24
Power & ammonia production with 2 E-SMR units
One SMR unit can supply power up to 453.8 tpd.

## Slide 25
Thermal to net electric, ammonia, and cogeneration efficiency

## Slide 26: Marginal break-even electricity price
(500 tpd nominal load)

## Slide 27: Maximized profits per market
(500 tpd nominal load)

## Slide 28: Mode of operation based on market volatility
Frequency of 2025 power prices in each market.
MBEP at nominal capacity (500 tpd) and an ammonia price of 700 €/t.
Norway
United Kingdom
Sweden
Poland

## Slide 29: Conclusion
Multiple SMRs are required to supply sufficient energy to the entire facility when ammonia capacity exceeds 453.8 tpd.
Cogeneration efficiency decreases with increasing ammonia production
At nominal capacity and an ammonia price of 700 €/t, ammonia production is more profitable than power production over 90% of the operating hours in the Norwegian market, 80% in the Swedish market, and 70% in the Finnish market.
Indicates that cogeneration of power and medium-scale ammonia production is more profitable compared to only power production in North Europe, and in other regions with similar low power prices, despite lower system efficiencies.

## Slide 30: Thank you

## Slide 31
Efficiencies (Gross electric production)

## Slide 32: Optimal ammonia capacity
(500 tpd nominal load)